## Slide 1: Concept Generation Theory of Inventive Problem Solving TRIZ in Russian
Notes: <number>

## Slide 2: TRIZ
A creative problem-solving methodology tailored for scientific and engineering problems
It is more structured and based on logic and data, not intuition or brainstorming
Hypothesis: There are universal principles of creativity that are the basis for creative innovations that advance technology
  Somebody someplace has already solved this problem (or one very similar to it.) Creativity is now finding that solution and adapting it to this particular problem
  Engineering ingenuity based on an inventory of ideas or a checklist
Notes: <number>

## Slide 3: TRIZ Problem Solution Process
General
Problem
Specific
Problem
General
Solution
Specific
Solution
Search for previously
solved problems
- 40 inventive principles
Identify analogies
Apply analogous solution
to my specific problem
Identify my problem
Formulate the problem through the prism of TRIZ
An example
Notes: <number>

## Slide 4: Five Levels of Problem Solution -based on patent literature
Routine design solutions using well known methods (30%)
Minor corrections to an existing system by known methods (45%)
Fundamental improvements to an existing system which resolve contradictions within the industry (20%)
Solutions based on application of new scientific principle to perform the primary functions of the design (4%)
Pioneering inventions based on rare scientific discovery (1%)
TRIZ deals mostly with design concepts at levels 3 & 4
Notes: <number>

## Slide 5: Primary Understanding
Problems and solutions are repeated across industries and sciences. The classification of the contradictions (technical or physical) in each problem predicts the creative solutions to that problem.
Patterns of technical evolution are repeated across industries and sciences.
Creative innovations use scientific effects outside the field where they were developed
Notes: <number>

## Slide 6: Problem-Solving Methodology
TRIZ uses a creative solution to overcome a system conflict or contradiction (improve some attribute of the system lead to deterioration in other system attributes) examples: reliability vs. complexity, strength vs. flexibility, etc.. Resolve contradictions due to “technical tradeoffs” (QFD can help)
Tabulation of the commonly used 39 engineering parameters in TRIZ
Application of 40 inventive principles
Notes: <number>

## Slide 7: Interactive TRIZ Matrix
Example: lengthen a static object without increasing weight. This is a contradiction. The improving feature is #4, “length of stationary object” and the worsening factor is #2, “weight of stationary object”. Use the matrix to discover possible ways of solutions, using the following inventive principles:
  35. Parameter changes
  28. Mechanics substitution
  40. Composite materials
  29. Pneumatics and hydraulics
Notes: <number>

## Slide 8: An example (http://www.ideationtriz.com/TRIZ_tutorial_1.htm)
Invention 3. Gripping workpieces of complex shape
To grip workpieces of complex shape, vice jaws must have a corresponding shape. It is expensive to produce
a unique tool for every workpiece, however.
Specific Problems to be resolved?
Shape, adaptability, stability
Notes: <number>

## Slide 9
Parameter to be improved/worsened:
  Stability of an object (with a better grip)  13
Worsening/improving parameter:
  Shape (cannot accommodate different or complex shapes) 12
  Adaptability  35
  From TRIZ table
  (13, 12) 1 (segmentation), 4 (asymmetry), 18, 22
  (13, 35) 2, 30, 34, 35
  (35, 13) 1,8, 15, 37
  (12,13) 1,4,18,33
Solution: Placing multiple hard bushings around the workpiece. The bushings can move horizontally to conform to the necessary shape.
Notes: <number>

## Slide 10: Physical Contradictions
Definition: a conflict between two mutually exclusive physical requirements to the same parameter of an element of the system.
Separation Principles
  Separation between time
  Separation between space
  Separation between the parts and the whole
  Separation upon condition (phase-transformation, physical-chemical-transformation)
Example: Liquid crystal film for privacy window. With current transparent, w/o current opaque
Other examples
Notes: <number>

## Slide 11: 39 Engineering Parameters
Weight of moving object
Weight of nonmoving object
Length of moving object
Length of nonmoving object
Area of moving object
Area of nonmoving object
Volume of moving object
Volume of nonmoving object
Speed
Force
Tension, pressure
Shape
Stability of object
Strength
Durability of moving object
Durability of nonmoving object
Temperature
Brightness
Energy spent by moving object
Energy spent by nonmoving object
  Power
  Waste of energy
  Waste of substance
  Loss of information
  Waste of time
  Amount of substance
  Reliability
  Accuracy of measurement
  Accuracy of manufacturing
  Harmful factors acting on object
  Harmful side effects
  Manufacturability
  Convenience of use
  Repairability
  Adaptability
  Complexity of device
  Complexity of control
  Level of automation
  Productivity
Notes: <number>

## Slide 12: 40 Inventive Principles
1. Segmentation
2. Extraction, Separation, Removal, Segregation
3. Local Quality
4. Asymmetry
5. Combining, Integration, Merging
6. Universality, Multi-functionality
7. Nesting
8. Counterweight, Levitation
9. Preliminary anti-action, Prior counteraction
10. Prior action
11. Cushion in advance, compensate before
12. Equipotentiality, remove stress
13. Inversion, The other way around
14. Spheroidality, Curvilinearity
15. Dynamicity, Optimization
16. Partial or excessive action
17. Moving to a new dimension
18. Mechanical vibration/oscillation
19. Periodic action
20. Continuity of a useful action
Notes: <number>

## Slide 13: 40 Inventive Principles
21. Rushing through
22. Convert harm into benefit, "Blessing in disguise"
23. Feedback
24. Mediator, intermediary
25. Self-service, self-organization
26. Copying
27. Cheap, disposable objects
28. Replacement of a mechanical system with 'fields'
29. Pneumatics or hydraulics:
30. Flexible membranes or thin film
31. Use of porous materials
32. Changing color or optical properties
33. Homogeneity
34. Rejection and regeneration, Discarding and recovering
35. Transformation of the physical and chemical states of an object, parameter change, changing properties
36. Phase transformation
37. Thermal expansion
38. Use strong oxidizers, enriched atmospheres, accelerated oxidation
39. Inert environment or atmosphere
40. Composite materials
Notes: <number>